# Requirements
- nRF Connect SDK
- Linux PC or Raspberry Pi (tested with Ubuntu 23.10)
- Bluetooth LE dongle or embedded controller
- nRF5340 DK – For the radio Co-Processor (RCP) device
- nRF DK compatible with matter accessory samples (e.g. nRF5340 or nRF52840)
# RCP Setup
Original instructions (1).
To use e DK as an RCP first we need to create a new nRF application project using the RCP sample from nrf/samples/openthread/coprocessor.
Once the project is created add the following config option to prj.conf.
CONFIG_IEEE802154=y
Then we need two new devicetree overlays, nrf5340dk_nrf5340_cpuapp.overlay and nrf5340dk_nrf5340_cpunet.overlay.
Create the cpuapp overlay to boards/nrf5340dk_nrf5340_cpuapp.overlay and add the following content to it.
/ {
chosen {
zephyr,console = &uart0;
zephyr,ot-uart = &uart0;
zephyr,shell-uart = &uart0;
zephyr,uart-mcumgr = &uart0;
zephyr,bt-mon-uart = &uart0;
zephyr,bt-c2h-uart = &uart0;
zephyr,bt-hci-rpmsg-ipc = &ipc0;
nordic,802154-spinel-ipc = &ipc0;
zephyr,ieee802154 = &ieee802154;
};
};

&ieee802154 {
    status = "okay";
};

Then create the cpunet overlay to child_image/802154_rpmsg/boards/nrf5340dk_nrf5340_cpunet.overlay and add the content below to it.
/ {
model = "Nordic nRF5340 DK NRF5340 Network";
   compatible = "nordic,nrf5340-nrf5340-cpunet";

chosen {
zephyr,console = &uart0;
zephyr,shell-uart = &uart0;
zephyr,uart-mcumgr = &uart0;
zephyr,bt-mon-uart = &uart0;
zephyr,bt-c2h-uart = &uart0;
zephyr,bt-hci-rpmsg-ipc = &ipc0;
nordic,802154-spinel-ipc = &ipc0;
zephyr,sram = &sram1;
zephyr,flash = &flash1;
zephyr,code-partition = &slot0_partition;
zephyr,ieee802154 = &ieee802154;
};
};

&ieee802154 {
status = "okay";
};
After this we can flash the device with the RCP project.
west build -p -b nrf5340dk_nrf5340_cpuapp
west flash
# Setting up OTBR (OpenThread Border Router)
Original instructions (2).
If you don’t have Docker installed yet install it with.
sudo apt update && sudo apt install docker.io
After installing docker start the docker service.
sudo systemctl start docker
Create an IPv6 network for the OTBR container in Docker.
sudo docker network create --ipv6 --subnet fd11:db8:1::/64 -o com.docker.network.bridge.name=otbr0 otbr
Clone the OTBR image.
docker pull nrfconnect/otbr:98dda6c
Load IPv6 filer module.
sudo modprobe ip6table_filter
Use the following command to run the otbr. Remember to change the baudrate and the serial port to the application cores serial port. The default baud rate on nRF5340 is 115200 and the application core is usually found as /dev/ttyACM1
sudo docker run -it --rm --privileged --name otbr --network otbr -p 8080:80 \
--sysctl "net.ipv6.conf.all.disable_ipv6=0 net.ipv4.conf.all.forwarding=1 net.ipv6.conf.all.forwarding=1" \
--volume /dev/ttyACM1:/dev/radio nrfconnect/otbr:98dda6c \
--radio-url spinel+hdlc+uart:///dev/radio?uart-baudrate=115200
Now create a new thread network, you can use the following instructions (3) or open the router’s configuration page on http://localhost:8080 and selecting “Form” in the side menu.
Note down the On-Mesh Prefix value (e.g. fd11:22::/64). Create a route in the ipv6 table using the On-Mesh Prefix.
sudo ip -6 route add fd11:22::/64 dev otbr0 via fd11:db8:1::2
Check the otbr status and the status of the thread node running in Docker.
sudo docker exec -it otbr sh -c “sudo service otbr-agent status”
sudo docker exec -it otbr sh -c “sudo ot-ctl state”
Next we can test the otbr with any matter sample that has configured connection handling
# Testing the OTBR with Thingy:53: Matter weather station
First start by flashing the thingy53 board with the application source code. Replace the project source location with nrf installation location.
west build -p -b thingy53_nrf5340_cpuapp ~/ncs/v2.6.0/nrf/applications/matter_weather_station
To make release build instead of debug use the following command instead.
west build -p -b thingy53_nrf5340_cpuapp ~/ncs/v2.6.0/nrf/applications/matter_weather_station -- -DCONF_FILE=prj_release.conf
After the build is finished flash it to the board.
west flash
Now we can add the device to the thread network with chip tool. First open the device’s serial monitor (this requires a debug build, release build does not expose a serial interface) remember to look up what port the device is connected, e.g. /dev/ttyACM2.
screen /dev/ttyACM2 115200

Now in the serial terminal we need to find the device discriminator and pin code. In the picture below the setup info is 0xF00 for discriminator and 20202021 for the pin code
Next get the dataset code from the otbr.
sudo docker exec -it otbr sh -c “sudo ot-ctl dataset active -x”
With this information we can open chip-tool and connect the device to the matter network. The pairing command has the following signature “pairing ble-thread <node-id> hex:<dataset> <pin_code> <discriminator>”
chip-tool interactive start
pairing ble-thread 0xf1 hex:0e08000000000001000035060004001fffe00708fdc10dceb1c0a3510c0402a0f7f8051000112233445566778899aabbccddeeff030e4f70656e54687265616444656d6f0410445f2b5ca6f2a93a55ce570a70efeecb000300000f0208111111112222222201021234 20202021 0xf00
Now the device should be connected to the matter network and we should be able to read some values from it
temperaturemeasurement read measured-value 0xf1 1
relativehumiditymeasurement read measured-value 0xf1 2
pressuremeasurement read measured-value 0xf1 3
# Sources
1. Nordic semiconductor 2024. Matter over Thread: Configuring Border Router and controller on one device. Search date 8.4.2024. https://docs.nordicsemi.com/bundle/ncs-latest/page/nrf/protocols/thread/tools.html#configuring_a_radio_co-processor.
2. Nordic semiconductor 2024. Thread tools. Search date 8.4.2024. https://docs.nordicsemi.com/bundle/ncs-latest/page/nrf/protocols/thread/tools.html#running_otbr_using_docker.
3. OpenThread 2023. Thread Border Router - Bidirectional IPv6 Connectivity and DNS-Based Service Discovery. Search date 8.4.2024. https://openthread.io/codelabs/openthread-border-router#2.
4. Nordic semiconductor 2024. Thingy:53: Matter weather station. Search date 8.4.2024. https://docs.nordicsemi.com/bundle/ncs-latest/page/nrf/applications/matter_weather_station/README.html#matter-weather-station-app.